## Slide 1
SKD072511-18 D40RWB241-F-T2
MANTA SOP

## Slide 2
1. Remove back cover screw/remove back cover
ATTENTION：1. The torque of the electric batch is 3.5 + / 0.5Kgf/cm2;You can't touch the COF.
Remove 6 pcs PA3*10 black screws
Remove 16 PCS KM3*6 black screws
(circle)

## Slide 3
The button position shall be stuck in place, and the PCB board shall be mounted on the button holder buckle
2.keyboard、IR board process
attention：1. Anti-static;2,IR board wire should be inserted in place；3. The button of the function bracket shall not be tilted or broken ；
Keyboard suit(P/N :AT0080258)
Function button holder
(P/N : AR0110096)
IR board suit(P/N :AT0090272)
Paste form on IR board（ P/N ： AS0030658 ），Align the cotton foam left side with the remote control board socket end edge
Insert IR board connect cabel(P/N::AE0041688
form(P/N :AS0030658)

## Slide 4
Attention ：1. The torque of the electric batch is 4.0 + / - 0.2Kgf/cm2
；
3. Lock speaker
The white line is on the left
Screw 4 pcsPWA4*13
White screw
PWA4*13 white screw(P/N :AS0010108)
Back cabinet(P/N :AR0020810)
Processed speaker
The red line is on the right

## Slide 5
EVA PAD(P/N :AS0030762)
attention： 1.EVA pad Must be attached;；
Stick 2 pcs 125*10*0.5mm EVA pad
NG
NG
OK
4.Paste EVA pad

## Slide 6
attention：1. The torque of the electric batch was 2.7 + / - 0.2Kgf/cm2.
Install the function key bracket
5.Lock keyboard bracket
Lock PWB3*6
White screw
PWB3*6 screw （ P/N :AS0010115）

## Slide 7
6. arrange the line on back cabinet
Attention ：1. Acetate tape should be attached tightly
Acetate tape 40MM
(P/N :AF0030368)
Align the horn terminal with the inner edge of the rear cover
6 sections of 40mm adhesive tape are pasted in the red square

## Slide 8
7.Insert pancel cable
Attention ： 1. Anti-static;You can't touch the COF.3. The screen line shall be inserted in parallel;4. Button the screen thread tightly ；
Stick 1 pcs60MM Acetate tape(P/N : AF0031369)
Insert panel cable(P/N : AE0042482)
Tear off the tape that holds the tube's extension cord

## Slide 9
8. Lock hexagonal bolt/ and terminal board-side
Attention ：1. The torque of the electric batch is 3.5 + / 0.5Kgf/cm2. can't touch the COF ；
锁两颗六角螺丝柱M3*4(料号: AS0020065)
锁两颗六角螺丝柱M3*6 (料号: AS0020034)
摆放侧端子板(料号: AW0041847)
Lock 2 cps Hexagonal bolt
M3*4(P/N : AS0020065)
Lock 2 cps Hexagonal bolt
M3*6 (P/N : AS0020034)
Put terminal board(P/N : AW0041847)
Hexagonal bolt
M3*4(P/N : AS0020065)
Hexagonal bolt
M3*6(P/N : AS0020034)

## Slide 10
9.Lock mainboard
attention：1. Anti-static;2. The torque of the electric batch is 3.5 + / 0.5Kgf/cm2;You can't touch the COF.
PWM3*6 screw(P/N : AS0010433)
3
mainboard (P/N : AE0011469)
2
Lock 4 pcs PWM3*4 white screw
1
4
Fix the floor and pull up 45 degrees

## Slide 11
10.Lock IR board /terminal board
Lock 1 pcsPA3*6 black scre
1
Lock 2pcs PWM3*4white screw
PWM3*4 white screw(P/N : AS0010430)
PA3*6 black screw(AS0010261 )
Install IR board suit
attention： 1. Anti-static;2. The torque of the electric batch is 3.0 + / 0.5Kgf/cm2;You can't touch the COF ；
install(P/N : AW0041848)
2
3
lock 2 pcs PWM3*4 white screw
Install side terminal board(P/N : AW0041847)

## Slide 12
11.Insert cable
Attention ：1. Anti-static;2. All wires shall be inserted in place;You can't touch the COF.
Insert panel cable
Insert the extension cord of the lamp
Insert power cable
Insert key board wire + IR board wire
Power cable P/N : （AE0041892)
The white dots on the screen end align with the "triangle" symbol of the motherboard

## Slide 13
12.Arrange cable
Attention ：1. Anti-static;2. Wire rod avoids the high pressure part;3. can't touch the COF.
40MM Acetate tape(P/N :AF0030368)
所有线材要避开高压部分6mm以上
所有线材要避开此螺丝孔
60MM Acetate tape(P/N :AF0030369)
蓝色框处贴3段60mm醋酸胶布
红色框处贴6段40mm醋酸胶布
按键板线端子与面壳边缘对齐

## Slide 14
13. Insert keyboard cable
Attention ：1. Electrostatic discharge;You can't touch the COF.3. The connection line should be inserted tightly;
The power cord passes through the rear cover hole from the outside to the outside
(P/N : AE0041892)
Insert keyboard cable

## Slide 15
14.insert speaker cable,and put the back cabinet
Attention ： 1. Anti-static;You can't touch the COF.3. The rear cover shall be in place ；
put Clamp plate(P/N :AR0150003)
Put back cabinet
Insert speaker cable

## Slide 16
15.ScreW back cabinetI
attention： 1. The terminal board screw shall be locked first;2. The torque of the electric batch is 3.5 + / 0.5Kgf/cm2 ；
Screw19 pcs KM3*6black screw(P/N :AS0010409)
KM3*6 black screw (P/N :AS0010409)

## Slide 17
Screw 6pcsPA3*10 black screw (P/N :AS0010262)
Screw 1pcsTA3*8 black screw (P/N :AS0010134)
attention： 1. 1. The terminal board screw shall be locked first;2. The torque of the electric batch is 3.5 + / 0.5Kgf/cm2 ；
TA3*8 black screw (P/N : AS0010134)
PA3*10 black screw (P/N :AS0010262)
16.Screw back cabinet II

## Slide 18
Thank!